## Slide 1
Remove the signal volage VCC pullup resistor to reduce the max signal volage to 3.3 V
I2C DS1307 RTC

## Slide 2
BeagleBone-Black
Arduino Uno/Nano
Raspberry PI
I2C DS1307 RTC
Other OT device micro controller
Set RTC Unit for OT/IoT Device

## Slide 3
I2C DS1307 RTC
BeagleBone-Black
I2C DS1307 RTC | BeagleBone-Black
SCL | P9-19 I2C_2_SCL
SDA | P9-20 I2C_2_SDA
VCC | P9-05 VDD_5V
GND | P9-01DGND
GPIO Connection

## Slide 4
I2C DS1307 RTC | Arduino Uno/Nano
SCL | Pin24 A5/D19 SCL
SDA | Pin25 A4/D18 SDA
VCC | Pin17 +5V
GND | Pin19 GND
GPIO Connection
I2C DS1307 RTC
Arduino Uno/Nano

## Slide 5
Raspberry PI
I2C DS1307 RTC
I2C DS1307 RTC | Raspberry PI
SCL | Pin5 GPIO 3
SDA | Pin3 GPIO 2
VCC | Pin4 5V Power
GND | Pin6 Ground